It's become necessary to lower the front end a bit. Converts often suffer from this and need an altitude adjustment. I have a front sub-frame with springs from an XJS with 4.0L I6 but it still sits too high

Much discussed here, one way to lower this type of Jag is to use spaces on the spring pan. 

What I used.

24 washers, 5/32 extra think 3/8 washers.
12 split lock washers, grade 8
12 bolts, 3/8-24 X 1 1/8 - grade 8
4 bolts, 3/8-24 X 3.5
4 nuts, 3/8-24 nylock
Total cost of hardware was about 50$

The washers were doubled up for a 5/16 inch pan drop. This resulted in a 1 inch drop at the fender lip. I've done this before using some crude cut steel bar, but the washers are a cleaner look and Just enough for my setup. I got 15 inches from the spindle center to the fender lip. This is the same measurement as my un-disturbed reference coupe. 
Great success. I dont want the car too low here in the herky jerky moonscaped roads of the big city.