THROTTLE POTENTIOMETER KIT

REPLACES EAC2670 on V12 and 3.6 ENGINES

- Disconnect throttle pushrods from throttle capstan.

- Disconnect 3 way plug connecting potentiometer to engine harness.

- Undo 4 off  7/16” AF nuts securing throttle capstan assembly.

- Remove nuts and washers and lift assembly off.

- Remove 3 screws securing potentiometer under capstan assembly.

- Engage new potentiometer spindle adaptor with capstan spindle and fasten in place with the 3 cap head screws provided.

- Connect the 3 wires to the harness plug according to the listing below.

- Switch on ignition, without starting engine, and using a voltmeter check that the signal output on the green wire is 0.32 volts (+ or - 0.02 volts) with the capstan wheel in the closed throttle position. Adjust as necessary via the 2 clamping screws.

- Reassemble by reversing operations 1-5 above.

Wire connections:-

Potentiometer                    3 Way Harness Plug                     Function

Red                                     Yellow/Pink                                    5 volts

Green                                  Yellow/White                                  Signal out

Black                                   Yellow/Black                                  0 volts